## Slide 1: HETS Horizontal Thrust Structure CDR
POCs:
Bhaskar Jain – Lead
Mohammed Al-Mahrouqi - RE

## Slide 2
Requirements & Considerations
Overview
Design & Analysis
  Thrust Structure
  Blast Sheild
Logistics
  Transportation
  BOM
  Timeline
Outline

## Slide 3
The system shall be capable of testing engines for the Daedalus vehicle
  The system’s thrust structure shall be able to support 10,000lbf of thrust*
    The thrust structure must not be the root cause of any engine anomalies
    The thrust structure shall allow for engines of different sizes and configurations to be mounted
    The thrust structure shall constrain off-axis force while allowing linear force data to be collected
    All components of the thrust structure shall have a minimum FOS of 3
    The thrust structure shall not apply the main thrust load directly to the system holding the fluids
    *Given testing site is unknown right now, concrete vs soil is the only thing not rated for this
HETS Requirements
Engine Testing Requirements

## Slide 4
The system shall support rapid engine testing
  The system shall be transportable to and from test sites potentially far from Atlanta
  The system must be capable of multiple hot fire tests in a single day
  The system shall be modular
    The thrust structure must have the ability to mount multiple engines of different sizes for testing purposes
    The system shall use standardized mounting systems to allow lines and components to be replaced
  The system must not require assembly at the beginning of each test
    All components of the system that are required to be insulated shall remain insulated if they are required on the system
Frequency Requirements

## Slide 5
Overall Requirements
  Horizontal
  Engine nozzle 1ft from ground for plume
  Can be mounted via earth anchors or concrete
  Engines up to 14” diameter
  Space for propellant lines and fittings
  Be able to test
      Subscale Heatsink, Ablative, Regen
      Vespula Heatsink, Ablative, Regen
      Darcy Space
Environmental Requirements
  Everything painted for corrosion resistance
  COTS parts are rated for outdoor usage
  Tarp to cover system
Other Considerations

## Slide 6: System Overview
I Beam will handle all deflection
Mostly welds
Fluids should mount easily
Main Features
  Railing
  Bearings
  Rings
  Brackets
  Ball Joints
  Load Cells
  I beam

## Slide 7: System Overview: Dimensions
Total height: 28.75”
Height from center of engine to ground: ~14.93”
Length: 63"
Width: 34.3”
Spacing of Earth Anchors: 14”
Estimated Total Mass 346.26 kg (+- 5%)
Blast Shield: 185.08576 kg
Ground Plates 56.44 kg
Others 104.72 kg

## Slide 8
Design: Rings
Two plates on the bottom, one on top
Shear Load of 1000lbf ;
Ring top max. deformation: 1.1605 in
Ring bottom max. deformation: .0042452 in
(won't really experience shear load, only vertical load)
3D printed spacer (with holes to screw everything in into)
Ring Bottom Piece
Ring Top Piece
1k lbf Vertical Load
1K lbf Shear Load
0.25”
0.125”
1K lbf Shear Load
1K lbf Shear Load

## Slide 9
Brackets
Motivation: need room for fluids, connects rings to Load Cell
Carbon Steel (waterjetting)
  Outer Arc: R 5.76”
  Inner Arc: R 3.26”
  Gap Width: 2.389”
  Top Hole: D 0.75”
  Side Holes: D 0.68”
Able to handle load?
  Euler Buckling on one segment, one fixed and one free end
  Pcr = 8290 lbf x 4 = 33160 lbf >> 10k lbf
5k lbf Normal Load

## Slide 10
304 Stainless Steel Rods from McMaster (2x~$50)
  Corrosion resistant up to 1500F
  2 Forces Loading Case: max deflection at L/2= .05in with 2000lbf (will likely be closer to 200-300lbf nominal)
    Deflection Calculations Lines 1-8
1" Bearings (4x~$100)
  Dynamic Load rating: 850lbf
    4x850=3500lbf >> 1000lbf off axis + ~200 lbf engine weight
  Self-aligning bearings compensate for shaft misalignment <= 1deg
COTS Bearings and Shaft

## Slide 11
Connect the rings to the bearings
Cantilevered Beam Analysis:
  1000lbf acting at the edge of the bracket: deflects ~0.002 in.
Close up of bolts attaching the bearings to the rings
  1000lbf per bolt, shear stress / bolt = (allowable stress = 40000 lbf/in^2)
Will mill these with angle iron stock
Bearing Brackets

## Slide 12
Screw holes are slotted so we can easily align the rods to make them parallel (if we machine things outside of 1deg tolerance)
¼-20 screws to bolt the rod to these shaft end supports
  For a 1000lbf load acting on just one of the bolts: 20ksi stress (65ksi allowable, FOS=2)
  1000 being distributed across 4 bolts. No chance of failure
Shaft end supports
  Made from 2x ½" carbon steel plates (cost optimal)
  First plate has a larger hole for the rod to sit on
Brackets
  Angle Iron
  Machining: mill
Shaft End Supports

## Slide 13
Ball Joint Rod End, 3/4"-16
  Rated for 15.850lbf ($15.33 per)
    Only really need to rate this for off axis forces, the 10,000 lbf would go axially through the rod, but other requirements drove the large size
  Requires lubrication
  Zinc plated: moderate corrosion resistance
Chose this size because it directly interfaces with the Load Cell
  Bolt Calcs: 65ksi allowed, FOS of 2
  ½" --> 51ksi stress / bolt ($10.20)
  ¼" --> 203ksi stress / bolt (would fail) ($5.43)
  ¾" --> 22ksi stress / bolt ($15.33)
Design has 2 in perpendicular directions so that the entire load of the engine is in one direction
  prevents off axis forces
  More accurate reading
Ball Joints

## Slide 14
Motivation: need to connect ball joint to I-beam
Analysis:
  3.6707e-004 in Max. Deformation for 10K lbf.
  1.8354e-004 in Mas. Deformation for 5K lbf considering 2 supports transmitting 10K lb. to I-Beam
  Threaded rod with nuts locking up the support with the ball joint.
Manufacturing:
  Connect three 1/8" plates together and then weld that assembly to the I-beam.
Design: Ball Joint Connector
10K lbf Load

## Slide 15
W8x24 I-Beam, 18" Long, ~$58.54, Ixx=82.8
  Cantilever beam deflection done on beam
  Deflection at 14in with 10,000lbf = .00544in ; 50,000lbf = .027in
    Even with any potential dynamic loading cases, this will be sturdy
    I Beam Deflection Calculations, Lines 9-16
  To account for I beam flange deflection, we will weld plates onto it, wherever the load is being attached.
    Euler Buckling on those flanges: Pcr = 408 Mlbf. Will not fail compared to 10klbf load max
    Calculations, Lines 17-20
I Beam

## Slide 16
1 10k lbf Load Cell mounted to prevent static indeterminacy
  Interfaces with our electrical system (already have 1)
  Rated for 10,000lbf ±0.02% ($380.25)
    Can safely go up to 15,000lbf without any failure
  Rated IP67: anti-corrosion
    No ingress of dust; complete protection against contact.
    Immersion up to 1m in water (will be fine outside)
Load Cell

## Slide 17: Ground Plate
Weld Calcs
  Assuming E60 electrode is used
  Top plate to main beams:
    Net force on each of four welds: 11.127N = 2.5014 kips
    Weld sizing: 0.5625 in. Fillet weld leg --> minimum 5/16"
    60 in. Weld on each side of main beams
      I-Beam:
        Net Force on welds = 10000 lbf
        Weld sizing: 0.39 in. - 0.6075 in. Fillet weld leg --> minimum 5/16"
        72.56 in weld

## Slide 18
18” Penetrators |  | 
Parameter | Value | Note
Length | 20” | Corrosion-resistant cast Aluminum
Diameter | 1 3/4” | 
Inclination Angle | 0 | Minimal soil disturbance (unlike helical anchors)
Spacing |  | Use wrench to install Two rows, with 5 anchors in ea.
Load |  | 
Parameter | Description | Note
Axial Load Capacity | 350 lbf (loose soil) vs 2500 lbf (grout/asphalt) | Per anchor Per anchor
Lateral Load Capacity | 510 lbf (loose soil) | Per anchor
Penetrators
Earth Anchors

## Slide 19
Earth Anchors
Assuming that EA Load is linearly corrrelated to volume:
  Max Load in loose soil with 3: 1530lbf; Max Load with 5 = 2287lbf.
  Same numbers for concrete. 3: 10925lbf and 5: 16332 lbf
For subscale testing, we can use soil, but for engines >1500lbf, we won't be able to.
  would need to pour our own concrete or find a testing site that has concrete we can go into

## Slide 20
Sizing Blast Shield
Calculating Initial Speed + Mass of Fragments
  Taken from NASA Paper, treating the engine like a pressure vessel
  Velocity = 270 m/s
  Mass = 80g
  KE = 2916J
Looking at equivalent plates for bullets:
  6.5 Creedmoor rounds with a KE of 3380J are stopped comfortably by a 3/8" steel plate
  5.56 rounds go through a ¼" steel plate with a KE of 1767J
  Therefore 3/8" is the minimum measurement for thickness

## Slide 21
Left top open to make room for plumbing
Plates are at an angle so fragments can be deflected and full force is not on the shield (also helps with blast wave)
Steel Plates are a big driver of cost
Just a bunch of carbon steel plate
Brackets can be angle iron
  Chopsaw to cut them to length and quick mill operation to make the holes
Will require 48 screws
Blast Shield Design

## Slide 22
Would need to separate the structure into multiple components to transport this
Ground plate would be one assembly
  Rods + bearings + rest of the engine carriage assembly would be the second part
This way we could assemble the plates and then screw the rest of the assembly together.
Transportation

## Slide 23
*already have Load Cell (around ~380)
BOM

## Slide 24
Total including Thrust Structure = $2190.64
BOM Blast Shield

## Slide 25
ANSYS Analysis – Check modes of vibration (first 6 should be 0)
  Expecting this to be fine
Ordering materials (lead times all within a week)
Building (1-2 weeks)
  Cutting/Welding
  Waterjetting
  Mill for any holes not done by waterjet
Next Steps

## Slide 26: Thank You!
Any Questions?

## Slide 27
BCs: Face welded to I beam is a fixed support
Appendix: Ansys sims
Ball Joint Connector
5K lbf Load applied on the surface area of the hole

## Slide 28
BCs: fixed support hole – transmitting force through it to the ball join then load cell
Appendix: Ansys sims continued
Engine to Ball Joint Support
5K lbf Load applied normally as shown

## Slide 29
BCs: bottom face is a fixed support assuming being held in place by bearing brackets
Appendix: Ansys sims continued
Ring Bottom Piece
1K lbf Load applied axially in shear to the inner surface

## Slide 30
BCs: holes of bolts are fixed support – assuming they are strong enough to handle the load
Appendix: Ansys sims continued
1K lbf Load applied axially in vertical direction to the inner surface upwards and downwards for the top face of the ends
Ring Bottom Piece
Stress intensity excluding the BCs

## Slide 31
1K lbf Load applied in shear to the inner surface
BCs: holes of bolts are fixed support – assuming they are strong enough to handle the load
Appendix: Ansys sims continued

## Slide 32
Added additional line of EAs in the soil
Only 10.85% interference
510 lb x 15 x .8915 =6,819.975 shear max load of EAs in soil
Appendix: Additional Earth Anchors

## Slide 33
simulation where we dont get the EAs in all the way, so instead of the whole depth being 18in, it becomes 14"
47.05% of the volume (15 EAs total) that it would normally affect
Very little interference, but much less volume = much less strength
6,819.975lbf * .4705 =3208lbf
Appendix: EAs Not All The Way In